## Slide 1: Introduction to AC performance
Jacques Wild

## Slide 2: Introduction to the flight planning optimiser
Short demo
Why we need aircraft performance data, numerical aspects

## Slide 3: Two types of aircraft
Data rich aircraft : General table containing all possible states to be flown are available.
Data poor aircraft : Only some speed modes are available, the speed of the aircraft is “fixed to these speed modes”

## Slide 4: What we are calculating
Basically, only two physical quantities are required in flight planning:
  Fuel flow (function of altitude, weight, temperature (in disa), speed (mach nb))
    In case of a data poor aircraft, the speed is “fixed” : handled as a three dimensional function in the code. The fuel flow in hence only available on a “per speed mode” basis.
    In case of a data rich aircraft, the speed can vary, handled as a fourth dimensional function in the code.
  Rate of climb/descent.
Additional quantities where interpolation is used for a data rich aircraft
  Speed limit : knowing the alt, the temperature and the weight of the aircraft, what is the authorised speed interval ?

## Slide 5: The BSAD format, our way of storing the ac perf data
Our format to store aircraft performance data.
Let’s have a look at an example. Different tables for data poor and data rich aircraft.
You will be given the specifications.

## Slide 6: Visualisation of the data
Demo

## Slide 7: For data poor aircraft
We are interested in the cruise fuel flow and the rate of climb of the aircraft that are 4-dimensional
getVal is the in-house function carrying out the interpolation/extrapolation
if (clb >= 0) {
perflets[clb].getVal(alt, disa, wght, z);
p.f.ffup = z[0]; //fuel flow
p.f.vxup = z[1]; //speed
p.f.rocup = z[2]; //rate of climb
}
if (crs >= 0) {
perflets[crs].getVal(alt, disa, wght, z);
p.f.cruiseFuelConsumption = z[0]; //fuel flow
p.f.tas = z[1]; //speed
}

## Slide 8: For data rich aircraft
We are interested in the cruise fuel flow and the drag of the aircraft (used to calculate the rate of climb) that are 4-dimensional
Drf Performance::cruisePerf(float alt, float disa, float wght, float mach)
{
dragFuel.getVal(alt, disa, wght, mach, udf.f);
// getVal does the interpolation, here what matters for the optimiser is the fuel flow and the drag
// udf.d.flow
// udf.d.drag
return udf.d;
}

## Slide 9: Loading aircraft performance data into the optimiser
const float minalt = 0;
const float maxalt = (npalt - 1) * 1000;
const float mindis = -15;
const float maxdis = 35;
const float minwind = pTab.ignore[3] ? 0 : -100;
const float maxwind = 100;
for (int i = 0; i < pTab.n[0]; ++i) {
for (int j = 0; j < pTab.n[1]; ++j) {
const float disa = mindis + disastep * j; //Atmos a(alt,disa);
for (int k = 0; k < pTab.n[2]; ++k) {
const float wght = minwght + wghtstep * k;
for (int l = 0; l < pTab.n[3]; ++l) {
const float wind = minwind + l * windstep;
ttt[tix++] = performance->getPerfFull(i * 1000.0, disa, wght, wind, sss);
}
}
}
}

## Slide 10: Data often available for a limited range or temperatures
As can be seen in the example of the speed limits, sometimes some extrapolation will be needed.
Same for the temperature (see previous slide). The optimiser produces a table for temperature between -15 and 35 even if the data is not available for these temperatures.

## Slide 11: Goals of the project
Parse the data files using python libraries (json, panda, …)
Research what libraries are relevant for 3 and 4 dimentional interpolation methods.
Implement interpolation methods for 3 dimensions (to be tested for speed limits for the data rich aircraft; fuel flow for cruise for the data poor aircraft) and for 4 dimensions (cruise fuel flow and drag for data rich aircraft).
Experiment with extrapolation.
Calculating rate of climb and testing the methods implemented above.